## Slide 1: Next Generation HPC architectures based on End-to-End 40GbE infrastructures
Fabio Bellini
Networking Specialist | Dell

## Slide 2: Next Generation HPC architectures

## Slide 3: WHY 10G Ethernet ?
Technologies Trend
  Multi-core processor Technology
  Converged Ethernet and FCoE
  Ip Storage
  Virtualization
  40Gb & 100Gb are now available
  10G Ethernet price point are dropping
  10G NICs
  Switch si below 500$ per port
  Very attractive price performance
  Lower opex and implementation costs
  Ethernet widly adopted: capitalize staff skill and management tools
  10G Ethernet technology has matured
  Reduced 10G internnection cost
  Banchmark data available
  Volume depolyment

## Slide 4: Is 10 Gigabit Ethernet Ready for HPC?
November 2008

## Slide 5: November 2011 10 Gigabit Interconnection
Interconnect | 2009 | 2010 | 2011
Gigabit Ethernet | 259 | 219 | 210
10G Ethernet | 1 | 7 | 14

## Slide 6: 10G Ethernet Issues
10G released 2002, What prevent faster adoption ?
  10 Gig NIC
  Price of Switch port
  Switch Scaling (single device)
  Media PYI limits & confusion
  Proof of Performance
  Architecture scaling

## Slide 7: 10G NIC
Price are dropping fast
New server stil support 1G, but has 10G as preferred interconnection
Multiple 10G ports per server/blade-server
Stable and mature for HPC application
TCP Off load Engine support, IWARP support

## Slide 8: Price of 10G Ethernet switches
Initial cost of 10G ports used to cost more than server !
10G Ethernet switch price < $500/port

## Slide 9: Switch Scaling
10G first released 2002
  max density per single device 32 10G ports line rate per device
  Nowadays single 1RU switch support up to 64 line rate 10G ports
    Single ASIC switch
    Sub uSec
    < 500Watt
    TOR
    Leaf in 2 Layer semplified Clos Architecture
  Chassis based devices able to scale up to few hundreds of 10G ports
    Crossbar Switch Fabric
    Clos Switch Fabric
    VOQ to prevent HOLB
    Single node 10G access Layer
    10G Aggregation Layer in 2 Layer architecture
    Spine in 2 Layer semplified Clos Architecture

## Slide 10: 10G Media PYI limits & confusion
STD C.Type Dst.
10GBase-CX4 15mt
10G SFP+ Direct Cable
  Passive 7mt
  Active 50mt
  10GBase-T cat6a/7 100mt
STD F.O. Type Dst.
10GBase-USR MM OM1,2,3 100mt
10GBase-SR MM OM3 300mt
10GBase-LRM MM OM1,2,3 220mt
10GBase-LR SM 10Km
10GBase-ER SM 40Km
10GBase-ZR SM 80Km
10GBase-LX4 MM/SM
10GBase-T
  Cat 6a/7
  Expensive
  Power hungry
  2,6uSec Latency
10G interconnection
Price reduction 10 to 1
SFP+ Direct Attached Cable
Passive/active cable with sfp+ end
High density same as rj45

## Slide 11: Proof of Performance
10G Ethernet offres:
  Same familiar operating enviromental ‘’evolving ethernet’
  Ease of use, debug and management
  Path to 40 and 100G Ethernet
  10x bandwidth and 8x better latency compared to 1G Ethernet
  Application performance proofed

## Slide 12: 10G Application proof of performance
10GE 32% Faster than 1G, for 32 cores case.
Pam CRASH: Elapsed time

## Slide 13: 10G Application proof of performance
10G 30% faster than 1G for 64 core case
RADIOSS 9.0: speed up

## Slide 14: Architecture Scaling
Legacy Clos architecture
  2 Tier Design Spine and leaf
  Meshed connectivity
  1:1 Bandwidth between the Spine and Leaf
  10G line rate access ports
  Multiple active uplink
  Predictable latency
Legacy CLOS topology
Interconnects Uplink
Spine
Up to 32
Leaf switches
Leaf
UP to 16 Spine Switchses

## Slide 15: Architecture Scaling Evolution
Legacy CLOS topology
Interconnects Uplink
Spine
Up to 32
Leaf switches
Leaf
UP to 16 Spine Switchses
One hop more..... From 2 to 3 layer
Layer 2
Resiliancy
Latency
Over Subscription
....

## Slide 16: Architecture Scaling Evolution Improve intra-chassis performance with local switching
Without Local Switching
All intra-chassis East-West traffic (blade-to-blade/VM-to-VM) sent to Top-of-Rack switch
Top-of-Rack Switch
West
East
With Local Switching
All intra-chassis East-West traffic processed locally for improved performance
Top-of-Rack Switch
West
East
= More ToR ports
4x fewer ToR ports
=

## Slide 17: Architecture Scaling Evolution Designed for efficiency: Reduce uplink ports & cabling with 40G
10G Connectivity
Using 10G port requires more ToR ports, more cables, more hassle
Top-of-Rack Switch
More ToR
ports @ 10G
=
40G Connectivity
Using 40G port requires less ToR ports, less cabling, less headaches
Top-of-Rack Switch
4x fewer ToR ports @ 40G
=

## Slide 18: Architecture Scaling Evolution
Legacy CLOS topology
40G Interconnects Uplink
Spine
Leaf
UP to 16 Spine Switchses
Up to 32
Leaf switches
Server scaling
  Up to 16 Enclosure
  4 x 40G uplink per enclosure
Load distribution based on OSPF ECMP
  Separate VLAN & Ip net for each enclosure
  Full network path redundancy
  No spanning tree
  Access OS from 1:1 to 4:1

## Slide 19: 40G ready & interoperable
IEEE 802.3ba 40Gb/s & 100Gb/s
  Standard approved June 2010
  Ethernet Alliance verified interoperability - June 2011 -
    Transceivers
      CFP MSA used for both 40 & 100 Gb/s
      QSFP+ used for 40Gb/s
    Optical cable
    Copper cable assemblies
      QSFP+ Direct Attach Copper
    Systems, including
      Test Systems,
      Switch/Router,
      Computer with HSE NICs

## Slide 20: Next generation HPC Architecture
Take Away
  10G is a mature proven technology ready for HPC
  Proof point emerging
  Banchmarks emerging
  10G Switching architecture are ready to scale
  To evolve next generation HPC
  40 G ethernet is ready proved and interoperable
  40G blade switch are ready to interconnect high density server blade enclosure
  40G 2 layer simplified architecture are ready to scale

## Slide 21: Thank You
Confidential